## Slide 1
A Novel Vapor Abatement Process for Low Concentrations of Mixed Toxic Gases.
Clinton Summers, Larry Shaffer, Joe Enneking and J. Louis Kovach
NUCON International, Inc.

## Slide 2: ORP Mission Need
DOE TOLD A FEDERAL JUDGE THAT USING SUPPLIED AIR RESPIRATORS TO PROTECT WORKERS FROM CHEMICAL VAPORS REDUCES EFFICIENCY BY 30 TO 70 PERCENT. Read more here: http://www.tri-cityherald.com/news/local/hanford/article84899392.html#storylink=cpy

## Slide 3: Current Headlines
More workers at Hanford report possible vapor exposure – Associated Press
Record number of Hanford workers sickened by toxic vapors – Channel 5, KING NBC affiliate
Feds will review Hanford response to toxic vapors – The Oregonian

## Slide 4: Fugitive Vapor Releases
Originate from the vapors in the head space of storage tanks
May be released due to temperature / pressure differences between the interior of the tank and ambient atmosphere
May be released during any activity that disturbs tank contents

## Slide 5: Fugitive Vapor Releases
Particulates
Air and water vapor
Inorganic compounds, Hg, N2O, NH3
Various volatile organic compounds (VOCS)
  Nitroso dimethyl amine
  Nitroso methyl ethyl amine
  Furans
  Other various organics

## Slide 6: Storage Tank (Chemical Reactor)
If ΔP ≈ 0 between tank head space and atmosphere, fugitive emissions ≈ 0, unless tank is disturbed
If ΔP is positive between tank head space and atmosphere, fugitive emissions > 0
Solids (sludge) layer
Liquid layer
Head space vapor layer

## Slide 7: Storage Tank
If ΔP is negative between tank head space and atmosphere, fugitive emissions will be 0
Influx of outside air (dilution air)
Solids (sludge) layer
Liquid layer
Head space vapor layer
Outside Air
Air + Contaminants

## Slide 8
Abatement Options
CARBON ADSORPTION
CONDENSATION
THERMAL AND THERMAL CATALYTIC
COLLECT
EMISSIONS
OXIDIZE VOCS
EMISSIONS
Carbon adsorption – good for VOCS and Hg
Condensation – not useful at very low VOC concentrations or in the presence of water vapor
Thermal – highly efficient removal of VOCS and nitrogen compounds
  DOES NOT work for Hg

## Slide 9: General Process
Remove water droplets
Reduce Relative Humidity
Catalytically treat any
Incomplete combustion
Products
Particulate “polishing”
HEPA Filter
Remove Hg
Combust VOCS and Nitrogen containing compounds using an internal combustion engine
Release to stack

## Slide 10: Typical Combustion Process
Most carbon is emitted as CO2 immediately.
A small fraction emitted as non-CO2 gases:
  CH4, CO, non-methane volatile organic compounds (NMVOCS)
  Ultimately oxidizes to CO2 in the atmosphere
Ammonia is combustible:
  4NH3(g) + 5O2(g) ---> 4NO(g) + 6H2O(g)
N2O is combustible:
  2N2O(g) --->2N2(g) + O2(g)
Notes: The flow can be thought of as a mass balance approach to tracking carbon through the process. You first determine the amount of carbon in the fuel, and then track its fate following the combustion process.

## Slide 11: Three Way Catalytic Converter
Reduction of nitrogen oxides to nitrogen and oxygen: 2NOx → xO2 + N2
Oxidation of carbon monoxide to carbon dioxide: 2CO + O2 → 2CO2
Oxidation of unburnt hydrocarbons (HC) to carbon dioxide and water: CxH(2x+2) + [(3x+1)/2]O2 → xCO2 + (x+1)H2O

## Slide 12: Unit Operations
Fresh air for start-up
Intake Air
Demister
Trap
Waste Storage Tank
Induce negative ΔP
Demist air stream, collect liquid water in trap / return to waste storage tank

## Slide 13: Unit Operations
Warm up stream to be treated, heat recovered from ICE
Mercury capture in fixed adsorbent bed (< 2.5 µg/m3)
HEPA
Intake Air from demister
Exhaust from ICE
To stack
Air/Air heat exchanger
Mersorb Bed
Hg Removal
To ICE

## Slide 16: System Advantages
Addresses the issue of fugitive emissions by maintaining a negative ΔP relative to atmosphere, clean air enters waste storage tank as contaminated head space air is removed
Removed head space air is treated to address all major contaminant issues; Hg, N2O, NH3 and VOCS using a proven technology
Optional “treatment nodes” to address future concerns
Economically viable, and at lower cost than other alternatives

## Slide 17: Operational Parameters
Gas temperature range
  Inlet to system: 57 to 115° F
  Mercury adsorbent bed inlet: ≈ 150° F
  ICE exhaust: 1200° F
  Exhaust to stack can be controlled if required
Mass flow range
  Demonstration unit: ≈ 30 SCFM
  Installed equipment: 30 to 2000 SCFM
Demonstration unit footprint
  7.5 x 10 ft

## Slide 18: Experimental Description
Process flow will be measured
Flow of contaminants will be set to pre-determined levels
Contaminant levels will be measured at process inlet
  IRPAD – organics, ammonia, nitrous oxide
  Lumex – mercury
Contaminant levels will be measured at process points down stream of adsorber and internal combustion engine outlets

## Slide 19: Experimental Set-up
Hg
Organic
solution
NH3
N2O
To process
Q ≈ 30 CFM

## Slide 20: Test Vapor Composition
Chemical Name | Target Inlet Concentration | Detection Method
Nitrous Oxide | ≈1000 ppm | IR-PAD
Ammonia | ≈ 400 ppm | IR-PAD
Mercury | ≈1000 µg/m | Lumex 915+
Formaldehyde | ≈10 ppm | IR-PAD
HexanesA | ≈ 200 ppm | IR-PAD
FuranA | ≈ 200 ppm | IR-PAD
2,3-dihydrofuranA | ≈ 200 ppm | IR-PAD
2-furan carboxy aldehydeA | ≈ 200 ppm | IR-PAD
PyridineA | ≈ 200 ppm | IR-PAD
Nitroso-dimethylamineB | ≈ 92 µg/L | IR-PAD

## Slide 21
Vapor Abatement Unit started and air flow through the system allowed to stabilize.
Exhaust backgrounds measured for at least 5 measurement cycles.
Inlet backgrounds measured for at least 5 measurement cycles.
Injection of challenge agent started, inlet concentration monitored until concentration stabilized.
Exhaust concentrations checked and monitored for at least 5 measurement cycles.
Injection stopped.
Vapor Abatement Unit allowed to “clear” for three to five minutes, then shut down.
General Testing Process

## Slide 22
Challenge Agent | Average Inlet Concentration (ppm) | Average Exhaust Concentration (ppm) | Remaining Challenge Agent Concentration (%) | Destruction Efficiency (%)
Ammonia | 424.08 | 7.74 | 1.83 | 98.17
Nitrous Oxide – Test 1 | 888.4 | 0.08 | 0.01 | 99.99
Nitrous Oxide – Test 2 | 1440.73 | 0 | 0 | 100
Formaldehyde – Test 1 | 4.27 | 0 | 0 | 100
Formaldehyde – Test 2 | 14.19 | 0 | 0 | 100
Organics Mixture | 304.89 | 14.55 | 4.77 | 95.23
NDMAB | 10.71 | 0 | 0 | 100
MercuryC | 2247C µg/m3 | 0 | 0 | 100